HUOM!!!!!!
    
         Ohjelma olettaa, ett{ hakemistosulkuina k{ytet{{n [] kirjaimia.
         se ei ymm{rr{ '<>' kirjaimia vaan menee niist{ sekaisin. 
         Ennen ohjelman ajoa pit{{ tarkistaa, ett{ oletushakemiston 
         nimess{ on oikeat sulut.

Introduction:

	The program TAR2VMS.C reads from a /foreign tape,or a file
which is an image of a Tar format tape, and extracts the files into 
a directory tree starting in the current default directory.
Directories will be created automatically.
For example, if your default is [JONES.MAIN], then the file
"electric/sub/test.c" will be written into [JONES.MAIN.ELECTRIC.SUB]TEST.C . 
	For the simplest operation, just  RUN it after defining the 
logical "TAPE" to be the the Tar source and doing a
MOUNT/FOREIGN/BLOCK=10240/RECORD=512 (if it is a tape); this
does the extraction automatically, reporting on stdout as it does.

	The extracted files will be written to your system as C stream files.
The VMS editor EDT will complain about the format, but EVE will not. 

	To convert a text file to standard VMS format:
(Thanks to Eric Gisin at U. of Waterloo:)
	You can use the VMS CONVERT utility by first creating a xxxx.FDL file
containing:

FILE
	ORGANIZATION		sequential
RECORD
	BLOCK_SPAN		yes
	CARRIAGE_CONTROL	carriage_return
	FORMAT			variable

Then run Convert with the regular DCL:
CONVERT/FDL=xxxx  input-file  output-file
-------------------------------------------------------------------------

Usage:

	-Define the logical variable "TAPE" to be the desired tape
	 unit or the file containing the Tar data.

	-Mount the tape /FOREIGN/BLOCK=10240/RECORD=512

	-Set the default directory below which the tree will be created
	 before calling the program. Thus: if your default directory
	 is SYS$SYSDEVICE:[MYDIRE], the file "electric/dbase.c" will
	 be written in SYS$DEVICE:[MYDIRE.ELECTRIC]DBASE.C

       -Then run TAR2VMS: (either by RUN or as a command)
	 if you use RUN, the operation is (extract, verbose)
	 otherwise:
'command' [options]
    	where the options are:
		"t" (listing only)	 Listing of files on tape 
		"x" (extract)		 Extract files from the tape 
		"v" (verbose):		 Report activity  
		"w" (wait)		 ...Not implemented
    -to use the options, the program must be executed using the 
     foreign command feature of VMS, by defining a command:
command :== $path:tar2vms      !where path=complete location of tar2vms.exe

	Example:
If the command is 'tar2vms', then:
tar2vms t 			will list the contents of the tar file
tar2vms xv			will extract all of the files, reporting

The listing reports the UNIX protection (in octal), the file size in bytes, 
the modification date on the tape, and the file name.

ERRORS: Most probable causes:
	"Can't open input file" - likely forgot to define TAPE, or mount
					the tape.
	"Error reading input"	- unexpected Tar format, or bad file.
	"Error writing output " - directory access error
	"Creation Error...   "  - illegal directory or file name

--------------------------------------------------------------------------
Important assumptions for this version (2.1):

    The defaults are (no options):
    -Extract all of the files, reporting as each file is created 

    -Read from a tape, mounted foreign, or a fixed record length
     file,with block size of 10240 bytes or less . If larger block 
     size, change the  definition of SIZE.

    -Stop on the special (blank header) block written by UNIX.
     (Note, like UNIX Tar, it does not move to the file mark at
     the end of the file. Answer "y" to the prompt to get to another
     tar file on the same tape.)THIS MIGHT NOT WORK...

    -All files are assumed to be UNIX stream and are 
     just copied. The vms file-attribute will be "stream". This may
     have to be changed in certain cases with CONVERT, or by writing
     a little C program to read the file and rewrite it.

    -When a UNIX linked file is encountered, there will be another
     file on the tape that contains the actual data. It may not be an
     earlier file that was the original file, since the files
     are written on in alphabetical order. The program will create a 
     file under the name of the linked file, but it will contain only
     a text messsage reporting the name of the file that contains the
     data.


    This version converts the path names to VMS format before creating
the files. Some special cases:

 (1) File names with more than one period (".") in the name have those
 	after the first converted to underscores (e.g. "mults.s.c" is
 	written out under the name "mults.s_c"
 (2) It is assumed that all of the pathnames on the Tar tape have
	complete directory info, with no device parts.
 (3) Commas and hyphens in file or directory names are converted to 
    	underscores. If this causes any problems, you can modify the
        code in vms_cleanup().Any such translations are reported in
	"verbose" mode.
 (4) Files are created with the user's default protection. The mode on
        the tape is ignored.
 (5) The dates of files extracted are the date of the extraction, not the
        date of the Tar version.
 (6) UNIX files that have no extension, and end in a letter will have 
	a "." added to the name automatically. This can cause some
	mysteries with large programs that look for other files with
	an exact string search. Also, if the files are written out
	to UNIX as a TAR tape from VMS, the "." goes along with the file
	name.

------------------------------------------------------------------------
Known Bugs:

    - Can't always read another file on the same tape. The program
      only works correctly when the tape had regular EOF marks on it,
      which apparently is not always true.
    - Can't selectively extract files from the tape. The "wait" option
      could be useful, but haven't got around to it..