HP48sx serial pinout

The following table shows how the 48SX 4 pin, the cable's 9 pin 
connector and the 25 pin adapter provided with the MSDOS PC link 
package are wired.

HP48SX                  IBM 9 PIN               IBM 25 PIN
(From the outside->in)
SHIELD-------------------1 SHIELD----------------  SHIELD
TX (Output)<-------------2 RX (Input)------------3 RX (Input)
RX (Input)-------------->3 TX (Output)---------->2 TX (Output)
SGND---------------------5 GND-------------------7 GND

Preston


Here are the pinouts for the 48SX serial port:



                  4 3 2 1
     /------------|-|-|-|----\
    |   48SX                  |    Pin   Function    Standard RS232 pin eqv.
    |   ___________________   |                       (25 pin connector)
    |  |                   |  |     1  Chassis Ground       1
    |  | 4:         "THIS" |  |     2  Transmit Data        2
    |  | 3:           "IS" |  |     3  Receive Data         3
    |  | 2:          "THE" |  |     4  Signal Ground        7
    |  | 1:       "SCREEN" |  |
    |   -------------------   |
    |                         |
    | [A] [B] [C] [D] [E] [F] |
    | MTH PRG CST VAR  ^  NXT |
    |     .  .  .  .  .  .    |

If you're making a cable, just make a standard null modem cable.
(reverse RX and TX)

      48SX pin           RS232 pin

   CHG   1  - - - - - - - -  1  CHG     Chassis ground does not
                                        actually have to be connected.
    TX   2  ------\ /------  2  TX
                   X
    RX   3  ------/ \------  3  RX

   GND   4  ---------------  7  GND

THORNTON JOHAN A